## Slide 1
Technical Design Thinking II
Spring 2025
LabVIEW – Conditional & Repetition Flow
Dr. Bruce McFall

## Slide 2
Important System Tasks
Color Sensors
  Horizontal and vertical positioning
  Calibration (all black and all white)
  Set-up code for calibration procedure
  Test materials for calibration procedure (Black and White cards)
Gyro Sensor
  Position
  Calibration based on device identifier (TBD)
  Set-up code for calibration procedure
Motors (Actuators)
  Test to compare output speed vs standard input control values
  Set-up code for calibration procedure and equivalent speed output
Robot Motion Modes
  Examine the motion of each of your possible modes
  Pay special attention to the effects the modes will have on the sensors
  Take into account all the tasks that will need to be performed
  Think about durability over the whole project

## Slide 3
LabVIEW – Conditional Flow
Logical operators (Boolean and Relational) can be found in the Boolean and Comparison areas of the Functions Palette
The Case Structure can be found in the Structures area of the Functions Palette
The Select function can be found in the Comparison area of the Functions Palette

## Slide 4
LabVIEW – Boolean Operators
For complex logical operations, you need to combine individual components with Boolean operators
Example: 0 < x <10
Translates into: 0 < x AND x < 10
AND
OR
NOT
NAND
NOR
Truth Tables
A and B
A or B
Not A

## Slide 5
LabVIEW – Case Structure
Once you’ve created your condition, you can use it to control how information flows through your Block Diagram using two structures:
  Case Structure
Change which case you see
True/False (If-Else)
Numeric (Case Structure)
Value = 0
Value = 1
Right click to add additional cases
Make sure one case
is default

## Slide 6
LabVIEW – Select Block
Once you’ve created your condition, you can use it to control how information flows through your Block Diagram using two structures:
  Select Block
  Allows you to select between two different flows

## Slide 7
LabVIEW – Repetition
All repetition structures are available in the Structures area of the Functions palette
Two types of loops available in LabVIEW to implement the two different types of repetition flow
  Counter-Based Flow: For Loop

## Slide 8
LabVIEW – While Loop
All repetition structures are available in the Structures area of the Functions palette
Two types of loops available in LabVIEW to implement the two different types of repetition flow
  Conditional-Based Flow: While Loop